## Slide 1: 2. Numbering systems
Subtitle
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2: Content
2.1 Introduction
2.2 Positional Number Systems
2.3 Conversion

## Slide 3: Objectives
After studying this chapter, the student should be able to:
Understand the concept of number systems.
Distinguish between non-positional and positional number systems.
Describe the decimal system (base 10).
Describe the binary system (base 2).
Describe the hexadecimal system (base 16).
Describe the octal system (base 8).
Convert a number in binary, octal, or hexadecimal to a number in the decimal system.
Convert a number in the decimal system to a number in binary, octal, or hexadecimal.
Find the number of digits needed in each system to represent a particular value.

## Slide 4: 1-Introduction

## Slide 5: 1- Introduction
A number system (or numeral system) defines how a number can be represented using distinct symbols.
A number can be represented differently in different systems.
For example, the two numbers (2A)16 and (52)8 both refer to the same quantity, (42)10, but their representations are different. This is the same as using.
Figure -2.1 Types of number system
Notes: 10-Thâp phân , 2-Nhị phân , 8-Bát phân , 16 – Thập lục phân

## Slide 6: 2 - Positional Number Systems

## Slide 7: Introduction
In a positional number system, the position a symbol occupies in the number determines the value it represents.
In this system, a number represented as:
has the value of:
in which S is the set of symbols, b is the base (or radix)
Notes: Base : cơ số

## Slide 8: The decimal system (base 10)
The word decimal is derived from the Latin root decem (ten). In this system the base b = 10 and we use ten symbols to represent a number.
The set of symbols is S 5 {0, 1, 2, 3, 4, 5, 6, 7, 8, 9}. As we know, the symbols in this system are often referred to as decimal digits or just digits.
In the decimal system, a number is written as:

## Slide 9: The binary system (base 2)
The second positional number system we discuss in this chapter is the binary system.
The word binary is derived from the Latin root bini (or two by two). In this system the base b 5 2 and we use only two symbols, S 5 {0, 1}. The symbols in this system are often referred to as binary digits or bits (binary digit.
Data and programs are stored in the computer using binary patterns, a string of bits.
Example 2.1 the number (101.11)2 in binary = 5.75 in decimal

## Slide 10: The hexadecimal system (base 16)
Problems :
The decimal system does not show what is stored in the computer as binary directly—there is no obvious relationship between the number of bits in binary and the number of decimal digits. Conversion from one to the other is not fast, as we will see shortly.
To overcome this problem, two positional systems were devised: hexadecimal and octal.
We first discuss the hexadecimal system, which is more common. The word hexadecimal is derived from the Greek root hex (six) and the Latin root decem (ten).
To be consistent with decimal and binary, it should really have been called sexadecimal, from the Latin roots sex and decem. In this system the base b 5 16 and we use 16 symbols to represent a number. The set of symbols is S 5 {0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F}.
Example 2.2 the number (2AE)16 in hexadecimal = 686 in decimal

## Slide 11: The octal system (base 8)
The second system that was devised to show the equivalent of the binary system outside the computer is the octal system.
The word octal is derived from the Latin root octo (eight). In this system the base b 5 8 and we use eight symbols to represent a number.
The set of symbols is S 5 {0, 1, 2, 3, 4, 5, 6, 7}. The symbols in this system are often referred to as octal digits
Example 2.3 the number (1256)8 in octal = 686 in decimal:

## Slide 12: Summary of the four positional systems
Table 2.1 Summary of the four positional number systems

## Slide 13: 3 - Conversion

## Slide 14: Introduction
We need to know how to convert a number in one system to the equivalent number in another system. Since the decimal system is more familiar than the other systems,.
First show how to covert from any base to decimal.
Then show how to convert from decimal to any base.
Finally, show how we can easily convert from binary to hexadecimal or octal and vice versa.
Notes: Quivalent ; tương đương , vice versa : ngược lại
Decimal system : hệ thập phân , hexadeciminal : lục thập phận , octal : bát phân

## Slide 15: Covert from any base to decimal
Figure 2.2 Converting other bases to decimal
Notes: Decimal point dấu thập phân

## Slide 16: Covert from any base to decimal (examples)
Example 3.1 Convert the binary number (110.11)2 to decimal: (110.11)2 = 6.75
Example 2.3 Convert the hexadecimal number (1A.23)16 to decimal : 1A.23 = 26.137

## Slide 17: Convert from decimal to any base.
We can convert a decimal number to its equivalent in any base. We need two procedures, one for the integral part and one for the fractional part.
Figure 2.3 Algorithm to convert the integral part
Convert 35 in decimal to binary.
Convert 126 in decimal to Octal.
Notes: Intergral : phần nguyên – fractional part : phần lẻ
Base : cơ số 10 , Quotient : hàm trả về phần nguyên của một phép chia

## Slide 18: Convert from decimal to any base (cont).
Convert decimal number 0.625 to binary
Convert 0.634 to octal using a maximum of four digits
Figure 2.4 Algorithm to convert the fractional part
Notes: Intergral : phần nguyên – fractional part : phần lẻ

## Slide 19: Binary–hexadecimal conversion
Figure 2.5 Binary to hexadecimal and hexadecimal to binary
Example 2.4
What is the binary equivalent of (24C)16?
Solution
Each hexadecimal digit is converted to 4-bit patterns: 2 → 0010, 4 → 0100, and C → 1100.
The result is (001001001100)2.

## Slide 20: Binary–octal conversion
Figure 2.6 Binary to octal conversion
Example 2.5
What is the binary equivalent of for (24)8?
Solution
Write each octal digit as its equivalent bit pattern to get (010100)2.
Notes: 3 bit trong hệ nhị phân gộp lại thành 1 chữ số trong hệ bát phân

## Slide 21: Octal–hexadecimal conversion
Figure 2.7 Octal to hexadecimal and hexadecimal to octal conversion